## Slide 1
NASA CMAPSS · IT 402 APPLIED FORECASTING METHODS
Aircraft Engine Failure Forecasting
FD004 DATASET
248 TRAINING ENGINES
Contributors:
U - Ummesalma Diwan (202518017)
D - Dhruv Parmar (202518030)
A - Aditya Jana (202518035)
S - Shrey Pandya (202518045)
Group - 13

## Slide 2
CONTEXT
The High Cost of Engine Failures
$500K+
Cost of a single unplanned engine removal
72%
Of aviation accidents involve mechanical failure
40%
Of maintenance costs are unplanned & reactive
Unplanned engine failures ground aircraft, disrupt schedules, and endanger lives. Predictive maintenance can shift the industry from reactive repair to proactive prevention.

## Slide 3
MOTIVATION
Why Predictive Maintenance
Avoid catastrophic failure — act before the engine reaches its end of life
Optimise maintenance windows — schedule downtime without over-servicing
Reduce fleet-wide cost — target only engines that actually need attention
Extend engine lifespan — data-driven decisions replace fixed intervals
Traditional Approach
Fixed-interval servicing — often too early (wasted cost) or too late (failure risk)
Predictive Approach
Forecast Remaining Useful Life (RUL) from sensor data — act precisely when needed

## Slide 4
PROJECT OVERVIEW
Project Overview
1
Load FD004 with unique engine IDs from NASA CMAPSS dataset
↓
2
Compute & cap Remaining Useful Life (RUL at 125 cycles), drop sensor leakage columns
↓
3
EDA + Preprocess — drop zero-variance sensors, cluster operating conditions (KMeans k=6), per-cluster StandardScaler, rolling features
↓
4
Build Health Index via PCA · Train classical models (AR, ARMA, ARIMA) · Train deep learning models (RNN, LSTM, GRU, Transformer)
↓
5
Evaluate with RMSE, NASA asymmetric score, R² · Compare all models

## Slide 5
DATASET
NASA CMAPSS Dataset
C-MAPSS : Commercial Modular Aero-Propulsion System Simulation
Simulates realistic turbofan engine degradation over hundreds of flight cycles
4 subsets (FD001–FD004) with varying operating conditions and fault modes
Each engine is run to failure — true RUL known from training data
This project focuses on FD004 — the most complex subset
Subset
Op Conditions
Fault Modes
Train Engines
FD001
1
1
100
FD002
6
1
260
FD003
1
2
100
FD004
6
2
248

## Slide 6
DATASET
FD004: The Hardest Dataset
248
Training engines
248
Test engines
61,249
Total training rows
Challenge 1: Six Operating Conditions
Engine flies at varying altitudes, speeds, and throttle settings. Sensor s3 (HPC temperature) reads 1590°R at sea level, 1420°R at altitude — same health state, different conditions.
Challenge 2: Two Failure Modes
HPC blade erosion (temperatures rise, pressure drops) OR fan degradation (vibration increases, efficiency drops). One model must learn both signatures simultaneously.

## Slide 7
DATASET
Dataset Structure
26 columns per row: 3 operational settings + 21 sensor measurements + engine ID + cycle
Each row = one flight cycle for one engine
Engines run from cycle 1 until failure (training) or truncation (test)
Test set is truncated — RUL must be predicted , not observed
RUL capped at 125 cycles — prevents dominance of long early-life phases
Column Group
Columns
Role
Engine ID
1
Unique engine identifier
Cycle
1
Flight cycle counter
Op Settings
op1, op2, op3
Operating condition
Sensors
s1 – s21
Physical measurements
RUL (computed)
1
Target variable

## Slide 8
CONCEPTS
Remaining Useful Life (RUL)
RUL = number of flight cycles left before the engine fails
Train set: true RUL computed from the maximum cycle per engine
Test set: RUL must be predicted at the truncation point
Capped at 125 cycles — early healthy cycles contribute equally
Ground truth provided separately as rul.txt for evaluation
RUL(cycle t) = max_cycle − t
125
Cap value
78
Mean test RUL
0
At failure

## Slide 9
PART 1
Exploratory Data Analysis
Understanding the data before modelling

## Slide 10
EDA
Engine Lifetime Distribution
248 training engines with lifetimes from 128 to 543 cycles
Mean lifetime: 246 cycles
Median: 234 cycles
All engines live longer than the RUL cap of 125 — cap is always effective
Minimum lifetime (128) > RUL cap (125)
Distribution is right-skewed — most engines live 150–300 cycles with a long tail

## Slide 11
EDA
Operating Conditions — 6 Distinct Clusters
op1: 536 unique values — continuous throttle setting (altitude-linked)
op2: 105 unique values — Mach/speed-related setting
op3: 2 unique values — altitude band (binary: ~60 or ~100)
The discrete clusters in histograms visually confirm 6 operating regimes
KMeans on (op1, op2, op3) separates these 6 conditions cleanly
Operating conditions cause large sensor jumps between consecutive cycles — not degradation. Clustering removes this confounding effect before modelling.

## Slide 12
EDA
Sensor Variance — Identifying Useless Sensors
s16, s10, s15 — near-zero variance; s16 variance = 0.000022
s9 — highest variance (113,520) — most spread, highly informative
Sensors with very low variance carry almost no information about degradation
Final drop decision combines variance + correlation + visual trajectory check
Decision
Sensors
Reason
DROP
s1, s5, s6, s10, s16, s18, s19
Near-zero variance + flat trajectory
KEEP
14 sensors
Visible degradation trend

## Slide 13
EDA
Sensor Correlation with RUL
Most sensors are negatively correlated with RUL — as engine degrades (RUL falls), sensor values rise
s14 has the strongest linear relationship (corr = −0.102)
s15 is the only positively correlated sensor (corr = +0.005)
Correlations are small — relationship is nonlinear, not captured by Pearson alone
Low Pearson correlation does not mean a sensor is useless — it means the relationship is nonlinear .

## Slide 14
EDA
Average Degradation Trajectories — 14 Retained Sensors
X-axis: normalised cycle (0 = engine start, 1 = failure)
s3, s4, s9, s11, s14 — clear upward trend as engine degrades
s7, s15, s17 — downward drift toward failure (sensors that fall with degradation)
Acceleration near failure (x > 0.7) is visible in many sensors — nonlinear

## Slide 15
EDA
Key EDA Insights
Engine Variability
Engine lifetimes range from 128 to 543 cycles. Models must generalize across very short and very long-lived engines.
Multi-Modal Operating Conditions
6 distinct operating regimes create sharp sensor jumps cycle-to-cycle.
Nonlinear Degradation
Average sensor trajectories show healthy phase followed by steep acceleration near failure.
EDA directly motivates every design decision: the 7-sensor drop, KMeans k=6, per-cluster scaling, health index, and the PCA detrending step.

## Slide 16
PART 2
Data Preprocessing
Setting up the sensor data for modelling

## Slide 17
PREPROCESSING
Dropping Useless Sensors
Of 21 sensors, 7 are near-constant across all rows
Standard deviation < 0.1 — they carry zero information about degradation
Keeping them adds noise to every model
Dropped: s1, s5, s6, s10, s16, s18, s19
14 sensors remain: s2, s3, s4, s7, s8, s9, s11, s12, s13, s14, s15, s17, s20, s21
7
Sensors dropped (near-constant)
→
14
Sensors retained (informative)
Variance-based selection

## Slide 18
PREPROCESSING
Operating Condition Clustering (KMeans)
Three operating columns (op1, op2, op3) define the flying condition each cycle
KMeans fitted on training data only — then applied to test data
Each row gets a label op_cluster ∈ {0, 1, 2, 3, 4, 5}
Fitting on training data ensures a consistent coordinate system across train and test
Why k = 6?
FD004 has exactly 6 distinct operating conditions. KMeans k=6 captures each condition as a separate cluster.

## Slide 19
PREPROCESSING
Per-Cluster StandardScaler
For each of the 6 clusters, compute mean & std of each sensor across training rows only
Removes altitude/speed baseline — what remains is deviation from normal
A healthy engine in any condition has sensor values near zero
A degrading engine has increasingly large z-scores — signal preserved, not clipped
scaled = (raw − cluster_mean) / cluster_std

## Slide 20
FEATURE ENGINEERING
Rolling Features
For each of 14 sensors: compute rolling mean and rolling std
Window sizes: 5 cycles and 10 cycles
Result: 14 × 2 (mean/std) × 2 (windows) = 56 rolling features
Sorted by (engine_id, cycle) first — prevents cross-engine contamination
Shared Conventions
Setting
Value
RUL cap
125 cycles
Sequence window (DL)
30 cycles
Train/val split
80 / 20 by engine_id
Random seed
42
Rolling windows
5, 10 cycles (mean + std)

## Slide 21
Evaluation Metrics
RMSE
√(Σ(pred−true)²/n)
Standard measure of prediction error in cycle units. Lower is better.
NASA
late: e^(d/10)−1 early: e^(−d/13)−1
Asymmetric — late predictions penalised more than early. Reflects real safety cost of missing a failure.
R²
1 − SS_res/SS_tot
Proportion of variance explained. 1.0 = perfect; <0 = worse than predicting the mean.

## Slide 22
PART 3
Building the Health Index
Compressing 14 sensors into one degradation signal

## Slide 23
HEALTH INDEX
Why We Need a Health Index
ARIMA is univariate
We have 14 sensor columns per row
Need one number that: starts near baseline when healthy, increases monotonically with degradation, and is comparable across all engines
The Goal
A single scalar that starts low (~−1) when healthy and rises monotonically toward ~3–4 at failure — for any engine, any operating condition
Why simple averaging fails
Different sensors move in opposite directions — s3 rises, s7 falls. Averaging cancels the signal. Picking one sensor misses the second failure mode.

## Slide 24
HEALTH INDEX
PCA: The Right Tool
PCA finds the direction in 14-dimensional sensor space where data varies the most
Since degradation drives the dominant variation, PC1 captures degradation better than any single sensor
FD004 subtlety: operating condition switching causes large sensor jumps — PCA would capture condition , not degradation
Fix: subtract per-cluster mean from each sensor before running PCA
The Critical Step for FD004
Subtract the per-cluster mean from each sensor before PCA. This removes the altitude/speed baseline. PCA then finds only the degradation direction in the residual.
After detrending: a healthy engine deviates near zero from its cluster's mean — in any condition. Degradation = increasing deviation from this zero baseline.

## Slide 25
HEALTH INDEX
Health Index: Step-by-Step
1
Rolling Mean Smoothing — replace each sensor with its 10-cycle rolling mean per engine (removes measurement noise)
2
Per-Cluster Mean Detrending — subtract each cluster's sensor mean; removes operating condition baseline
3
Global PCA on Detrended Sensors — first principal component (PC1) is the degradation direction
4
Sign Flip — if PC1 is negatively correlated with −RUL, multiply by −1 so higher = more degraded. Always.
5
Standardisation — normalise using training mean/std only (no leakage); healthy ≈ −1, near failure ≈ 3–4
6
Isotonic Regression — enforce monotonic non-decrease (physical reality: engines do not self-repair)

## Slide 26
HEALTH INDEX
Health Index in Action — Three Engines
All engines start near −1.0 (healthy baseline)
All engines end at 2.0–3.5 (severely degraded, near failure)
Shape: long flat healthy phase → steep acceleration near failure
Engine lifespans: 305–325 cycles — each engine is unique
Monotonic rise confirmed — isotonic regression worked correctly
Health index range: [−1.597, 4.402] · Failure threshold = 1.685

## Slide 27
HEALTH INDEX
Failure Threshold Selection
Threshold = value below which 95% of near-failure rows lie
Near-failure defined as RUL ≤ 5 cycles
Chosen threshold (q=0.05): 1.685
Only 22 of 248 test engines (9%) ever reach it in observed history — most are truncated early
This is why a fallback mechanism is required for 91% of engines
Quantile
Threshold
Test engines reached
q=0.05 ✓
1.685
22 / 248 (9%)
q=0.10
1.747
20 / 248 (8%)
q=0.20
1.840
17 / 248 (7%)
q=0.50
2.166
13 / 248 (5%)
q=0.70
3.363
0 / 248 (0%)

## Slide 28
PART 4
Classical Time Series Models
AR · ARMA · ARIMA on the Health Index

## Slide 29
CLASSICAL MODELS
ARIMA Framework
ARIMA doesn't predict RUL directly — it forecasts the Health Index forward
RUL = number of forecast steps until Health Index ≥ 1.685
Three parameters define the model:
p
AR order — how many past values to use for prediction
d
Integration order — how many times to difference for stationarity
q
MA order — how many past forecast errors to use for correction
Forecast → RUL Conversion
1. Observe health index up to cycle T
2. Fit ARIMA(1,2,1) on observed series
3. Forecast 150 steps forward
4. Find first step where h.i. ≥ 1.685
5. That step number = predicted RUL

## Slide 30
CLASSICAL MODELS
Finding d: ADF Stationarity Test
ARIMA requires stationarity — constant mean and variance over time
Health index clearly trends upward — non-stationary at level
ADF test (Augmented Dickey-Fuller): p < 0.05 → stationary, stop differencing
First difference removes linear trend (d=1); second difference removes acceleration (d=2)
FD004: 206/248 engines need d=2 — degradation accelerates
ADF Results — Engine 118 (543 cycles)
Level
ADF p-value
Verdict
Raw (d=0)
1.000
NON-STATIONARY
Diff-1 (d=1)
0.974
NON-STATIONARY
Diff-2 (d=2)
0.000
STATIONARY
→ Modal d = 2 across 248 training engines

## Slide 31
CLASSICAL MODELS
Raw vs. After First Differencing
Left (d=0): clear upward drift — non-stationary; ADF p=1.0
Right (d=1): linear trend removed; but variance spreads at higher indices — still non-stationary; ADF p≈0.97
FD004 degradation accelerates near failure — rate of change itself trends upward
Second difference (d=2) (acceleration of health index) becomes approximately constant → stationary

## Slide 32
CLASSICAL MODELS
Finding p and q: ACF / PACF (Twice-Differenced Series)
ACF : correlation at each lag → guides q (MA order). Cuts off → pure MA
PACF : removes indirect effects → guides p (AR order). Cuts off → pure AR
Large spike at lag 1 in both ACF and PACF (~−0.5) — introduced by double-differencing
After lag 1: bars mostly inside confidence band → MA(1) dominant structure
Both tailing off → mixed ARMA → ARIMA(1, 2, 1)

## Slide 33
CLASSICAL MODELS
AIC Grid Search — Final Model Orders
Every (p,q) combination tested on 15 representative training engines
Modal winner across 15 engines is chosen as final order
AR: p=10 wins— 10 past cycles carry predictive information
ARIMA: (p=1, q=1) wins — MA error-correction is the dominant structure
Final Model Orders
Model
Order
Interpretation
AR
(10, 2, 0)
10 lagged values, 2 differences
ARMA
(1, 2, 1)
1 AR + 1 MA term, 2 differences
ARIMA
(1, 2, 1)
MA error-correction dominant

## Slide 34
CLASSICAL MODELS
Residual Diagnostics — ARIMA(1,2,1)
QQ Plot (left): heavy tails — kurtosis = 7.95 vs 3 for normal. Occasional large errors expected
Residuals over time (right): fluctuate around zero; initial spike = model warm-up
Ljung-Box test: all p-values near 0 — residual autocorrelation remains
Imperfect residuals are acceptable: our goal is long-horizon RUL estimation , not perfect one-step forecasting. Rolling RMSE of 0.028 confirms practical usability.

## Slide 35
CLASSICAL MODELS
Rolling Forecast Validation — Engine 118
Blue line: observed health index (543 cycles)
Orange dashed: AR(10) walk-forward rolling forecast (last 30%)
Red dashed: failure threshold = 1.685
Rolling RMSE = 0.028 — one-step-ahead accuracy
Forecast crosses threshold at cycle ~480

## Slide 36
CLASSICAL MODELS
The Main Mechanism
RUL = slope × health_index + intercept
Safety factor 0.88 applied — makes all predictions slightly conservative
Why the Safety Factor?
NASA scoring penalises late predictions more than early ones. A 0.88 multiplier shifts all predictions slightly downward — accumulating fewer late-prediction penalties.

## Slide 37
CLASSICAL MODELS
Classical Model Performance
Model
RMSE
NASA Score
R²
AR(10,2,0)
27.67
25,742
0.586
ARMA(1,2,1)
26.19
17,514
0.629
ARIMA(1,2,1)
24.76
13,791
0.668
Adding the MA term (q=1) allows error-correction — ARIMA outperforms both AR and ARMA on all metrics.
ARIMA(1,2,1)

## Slide 38
PART 4
Deep Learning Models
RNN · LSTM · GRU · Transformer

## Slide 39
DEEP LEARNING
Why Deep Learning?
Classical models are univariate & linear — work on health index only
Deep learning uses all 14 sensors simultaneously — no information compression
Can learn complex, nonlinear mappings from sensor patterns to RUL
Designed for sequential data — temporal dependencies propagated through time
Trained on all 248 engines at once — learns a universal degradation model
Feature Engineering for DL
14 sensors × 3 rolling windows (5, 10, 20 cycles) = 42 features per cycle
Rolling means embed multi-scale temporal context at each step
Sliding window of 30 cycles → one input sequence per sample
Train/val split: 80/20 by engine_id (not by row — prevents leakage)

## Slide 40
DEEP LEARNING
RNN (Recurrent Neural Network)
Simplest sequential model — passes hidden state forward each cycle
Suffers from vanishing gradient — struggles to retain long-range information
Fastest to train — good baseline for comparison

## Slide 41
DEEP LEARNING
LSTM (Long Short-Term Memory)
Introduces forget, input, and output gates — learns what to retain and discard
Solves the vanishing gradient problem — can remember dependencies over hundreds of cycles
Particularly well-suited for long engine degradation sequences

## Slide 42
DEEP LEARNING
GRU (Gated Recurrent Unit)
Simplified LSTM — merges forget and input gates into a single update gate
Fewer parameters → faster training, often comparable performance to LSTM
Strong choice for shorter sequences or when training time is a constraint

## Slide 43
DEEP LEARNING
Transformer
Uses self-attention — each cycle can directly attend to any other cycle in the window
No recurrence — processes sequence in parallel; faster training on GPUs
Best at capturing long-range dependencies without gradient issues
More parameters → needs more data to generalise well

## Slide 44
PART 5
Quantile Regression Models
Probabilistic forecasting with uncertainty bounds

## Slide 45
QUANTILE MODELS
Quantile Regression: Beyond Point Estimates
Classical & DL models give a single point estimate of RUL
Quantile regression gives a distribution — lower bound, median, upper bound
Critical for safety: "We are 90% confident the engine will last at least X more cycles"
Conservative (lower quantile) predictions → schedule maintenance with a safety margin
Enables risk-aware decision-making across the fleet
Why Uncertainty Matters
A prediction of "50 cycles" hides whether the true value could be 20 or 80. Quantile models expose this uncertainty so operators can act conservatively.
Pinball Loss
Quantile models are trained with the pinball (quantile) loss — an asymmetric loss that penalises underprediction at upper quantiles and overprediction at lower quantiles.

## Slide 46
QUANTILE MODELS
Quantile Forecast Examples — Probabilistic RUL Bounds

## Slide 47
PART 6
Results & Conclusions
key findings

## Slide 48
RESULTS
Key Findings
ARIMA beats AR and ARMA — the MA error-correction term is critical for FD004's accelerating degradation
d=2 is essential — FD004 degradation accelerates, not just trends — two differences required for stationarity
Per-cluster detrending is the most important preprocessing step — without it, PCA captures operating conditions, not degradation
Conservative bias (safety factor 0.88) aligns with NASA's asymmetric scoring — early predictions penalised less than late ones
Deep learning captures multi-sensor interactions that classical univariate models fundamentally cannot

## Slide 49
Thank You